## Slide 1: Memory

## Slide 2: Memory
Memory: Part of the computer where programs and data are stored
Consist of a number of cells (or locations), each of which can store a piece of information
Each cell has a number, called its address, by which programs can refer to it
If a memory has n cells, they will have addresses 0 to n − 1
All cells in a memory contain the same number of bits

## Slide 3: Memory Example

## Slide 4: Memory Classification

## Slide 5: Memory Hierarchy
Fastest access, Most expensive
Slowest access, Least costly

## Slide 6: Cache Memory Placement

## Slide 7: Technologies used in Memory Design
Types of memories
  Random Access Memory (RAM): Memory from where data can be read and where data can be written – Volatile
    Static RAM (SRAM)
    Dynamic RAM (DRAM)
  Read Only Memory (ROM): Memory from where data can be read, but not where data can be written
    Useful for booting up, fixed data

## Slide 8: DRAM versus SRAM
Used as cache memory

## Slide 9: RAM versus ROM

## Slide 10: PROM
PROM (Programmable ROM) allows companies to write to the ROM chip once, not at the time of chip manufacturing
  Example: A washing machine manufacturer can buy ROM chips and write its instructions on the chip

## Slide 11: Auxiliary Storage
Auxiliary storage, also known as secondary memory or external storage, refers to the non-volatile storage devices that retain information even when the power supply is disconnected
Examples: HDD, SSD, Flash memory, Optical storage

## Slide 12: Hard Disk Drive (HDD)
Mechanical storage devices
Use magnetic material to store data
High capacity, low cost
These days replaced by SSD

## Slide 13: Flash Memory
Non-volatile memory
Retains data even when there is no power supply
Used in Solid State Drives (SSD), USB drives, memory cards
Low power consumption and durable
Other varieties: NAND flash memory or NOR flash memory

## Slide 14: Solid State Drive (SSD)
Use NAND flash memory
Faster, more durable

## Slide 15: Optical Storage
CD-ROM, DVD, Bluray disks
Magnetic disk contains information
Used more for music, movies, etc

## Slide 16: Memory Interleaving
Memory interleaving: Improve memory access performance by distributing data across multiple memory modules or banks or interleaves
Example: If we have two memory modules, the memory space might be divided into two interleaves: Interleave 0 and Interleave 1
Uses round robin algorithm
Parallel memory access possible
More useful in multi-core processors

## Slide 17: Memory Interleaving Example
Suppose we decide to use 4 interleaved memory modules
  Module 0 will contain memory addresses 0, 4, 8, 12, 16, …
  Module 1 will contain memory addresses 1, 5, 9, 13, 17, …
  Module 2 will contain memory addresses 2, 6, 10, 14, 18, …
  Module 3 will contain memory addresses 3, 7, 11, 15, 19, …
Advantage: The CPU(s) can read memory modules one after the other quickly to access data. For example, suppose an instruction needs data from memory locations 2 to 9. The CPU can quickly go to memory module 2, then to 3, then to 1, then to 2 again, etc.

## Slide 18: Virtual Memory and Paging

## Slide 19: Machine Language Instructions in a Process
Example of Process P1:
Address 0: 0011 0000 0000 0000
Address 1: 0010 0010 0000 0110
Address 2: 0110 0100 0100 0000
Address 3: 0000 0100 0000 0101
Address 4: 0001 0010 0110 0001
Address 5: 0000 1110 0000 0001
Address 6: 1111 0000 0010 0101
Example of Process P2:
Address 0: 1111 0000 0010 0101
Address 1: 1110 0010 0001 1110
Address 2: 1100 0101 0100 1100
Address 3: 1100 1000 0010 0001
Address 4: 0001 0010 0110 0001

## Slide 20: Process Addresses and Memory Addresses
Memory has cells, numbered using addresses
Example:
Memory address | Contents
0 | …
1 | …
2 | 
3 | 
4 | 
5 | 
6 | 
7 | 
8 | 
9 | 
10 | 
11 | 
12 | 
13 | 
14 | 
15 | 
16 | …

## Slide 21: Accommodating Multiple Processes in Memory
Memory address | Contents
0 | 0011 0000 0000 0000
1 | 0010 0010 0000 0110
2 | 0110 0100 0100 0000
3 | 0000 0100 0000 0101
4 | 0001 0010 0110 0001
5 | 0000 1110 0000 0001
6 | 1111 0000 0010 0101
7 | 
8 | 1111 0000 0010 0101
9 | 1110 0010 0001 1110
10 | 1100 1000 0010 0001
11 | 0001 0010 0110 0001
12 | 0001 0010 0110 0001
13 | 
14 | 
15 | 
16 | …
Process P1
Process P2
Process P1’s addresses and real memory’ addresses map one-to-one
But Process P2’s addresses 0 to 4 are mapped to real memory addresses 8 to 12

## Slide 22: Virtual Memory: Need
Physical memory (RAM) size = 4096 bytes
Process needs ~1 MB
Solution: Bring only 4096 bytes of addressable memory (process data) into the physical memory at a time and keep the rest in secondary storage
Example:
0 to 4,095 OR
4,096 to 8,191 OR
8,192 to 12,287
etc
Addressable memory (Process memory)
Available memory (RAM)

## Slide 23: Terminology
Process memory: Locations 0 to ~1 MB: Virtual address space
Real physical memory/RAM: Locations 0 to 4095 (Physical address space)
Page table or Page map table: Maps virtual address to physical address
Result: Virtual memory

## Slide 24: Virtual Memory: Modernization
Now, physical memory is much more than 4096 bytes (e.g. 8/16 GB)
It is logically divided into page frames
Example: One page frame = 1 MB
So, number of page frames = 16 GB / 1 MB = (16 * 1024) / 1 = 16,384
Process memory is divided into virtual pages
Some virtual pages are loaded into page frames, and the remaining ones are in the secondary memory
See next slide

## Slide 25: Page Mapping Table or Page Table
Virtual memory
Physical memory

## Slide 26: Page Replacement – Basic idea
Page fault: Program refers to a virtual memory address that is not present in the physical/real main memory
Working set: Set of pages that a program is actively and heavily using
Page replacement policy: Decides how to handle page faults
  Least Recently Used (LRU): Evicts the page least recently used
  First In First Out (FIFO): Removes the first loaded page
Thrashing: A program that generates page faults frequently
Demand paging: Load pages only on demand, not in advance
Dirty bit: Tells the OS if the page contents were modified, so as to not lose the changes in the event of page replacement

## Slide 27: Associative Memory
Associative memory: Also called Content-Addressable Memory (CAM)
Allows data to be retrieved based on its content rather than its specific memory address
Search keywords/patterns and stored with the data
We search for content or pattern, instead of providing memory address
Parallel search is possible: High performance
No need to sequentially look up memory addresses, so fast
Used in cache memory, network routers and applications where fast search is needed