## Slide 1: The ‘Bus’ Concept

## Slide 2: Computer Bus
Computer bus: A communication link (set of wires) used inside a computer to send data, addresses, control signals, and power to various hardware components
Buses connect various hardware components to each other
Main bus types: Connect CPU to RAM
  Address bus: Used for specifying memory addresses for reading or writing of data (Unidirectional)
  Data bus: Specifies data to be written or contains data that was read (Bidirectional)
  Control bus: Used for passing control signals (Bidirectional)
Address bus + Data bus + Control bus = System bus

## Slide 3: How is the System Bus Used?
Suppose the CPU wants to write a value of 0 in memory location 125
  Address bus = Specifies the address of the memory location
  Data bus = Specifies the data to be written
  Control bus = Specifies the write operation

## Slide 4: How is the System Bus Used?
Suppose the CPU wants to read data stored in memory location 125
  Address bus = Specifies the address of the memory location
  Control bus = Specifies the read operation
  Data bus = Will contain the data read from memory location 125

## Slide 5: Instructions
Data bus = Transfer data from the CPU to the main memory or from the main memory to the CPU
Remember, code is also in the main memory
CPU needs to fetch each instruction from the main memory and execute it
Which bus will be used to fetch the instructions from the main memory into the CPU?

## Slide 6: von Neumann versus Harvard Architecture
von Neumann Architecture
  Single memory for data and instructions
  Single bus
  Simple, Inexpensive
  Simultaneous multiple memory fetches not possible
  von Neumann bottleneck: Separation of memory and data
Harvard Architecture
  Separate memory and separate bus for data and instructions
  Multi bus
  Complex, Expensive
  Simultaneous two memory fetches possible
Data and Instructions Bus
Data Bus
Instructions Bus

## Slide 7: PCI Express
Earlier: Each component/device was connected to every other device using a separate wire (Point-to-Point connection)
Now: A common bridge connects various devices (Multi-Point connection)
Earlier Peripheral Component Interconnect (PCI)
Now PCI Express = Modern technique used for system bus
The CPU, memory, and cache are connected to a bridge chip
A switch is connected to the bridge
Each I/O chip has a dedicated point-to-point connection to the switch
Each connection consists of a pair of unidirectional channels, one to the switch and one from it
All the devices are treated equally
Works like a packet switching network

## Slide 8: Point-to-Point versus Multi-Point Connection
Point-to-Point
Multi-Point
Device A
Device C
Device B
Device D
Device A
Device C
Device B
Device D

## Slide 9: PCI Express

## Slide 10: Inside the CPU

## Slide 11: CPU Organization
CPU = CU + ALU + Registers
CU = Control Unit
ALU = Arithmetic and Logical Unit
Registers = Fast memory inside the CPU

## Slide 12: Registers
Register: Fastest type of memory, because it is inside the CPU
Purpose: Perform all arithmetic and logical operations in a computer
The original Intel CPU had very few registers, e.g.
  AX The accumulator register
  BX The base address register
  CX The counting register
  DX The data register
  IP Points to the next instruction to be executed (along with CS)
  Flags Contains results of a comparison

## Slide 13: Registers in x86 CPU

## Slide 14: Registers in x86 CPU
Size of each register = 16 bits
Four general-purpose registers (AX, BX, CX, DX) = Made of two separate 8-bit registers (high and low)
  Example: If AX = 0011000000111001 then AH = 00110000 and AL = 00111001
Four segment registers: CS, DS, ES, SS
  Code Segment (CS): Points to the segment containing the current program
  Data Segment (DS): Points to the segment containing the data being used
  Extra Segment (ES): To be used by the programmer as needed
  Stack Segment (SS): Points to the segment containing the stack

## Slide 15: Arithmetic and Logical Unit (ALU)
Arithmetic and Logical Unit (ALU): Performs most of the operations
Example: Add 5 to the accumulator register AX:
  Copy AX into ALU
  Send 5 to ALU
  Instruct the ALU to add these two values together
  Move the result back into the AX register

## Slide 16: Control Unit (CU)
Instruction Pointer (IP) or Program Counter (PC): Contains the address of the next executable instruction
Fetch instruction code (op code) from the memory using PC
Move the op code into the instruction decoding register (Instruction Register (IR))
Increment the value in IP/PC to get the next instruction after the current instruction is complete

## Slide 17: Instruction Set Architecture (ISA)
Every CPU understands a fixed set of machine language instructions = Instructions set
Called Instructions Set Architecture (ISA)
Different CPU families (e.g. Intel, ARM) = Different ISA
Meaning: Intel CPU’s machine language ≠ ARM’s machine language

## Slide 18: Op Code and Operands
Instruction: Also called as mnemonic has two parts:
  Op code: Operation/instruction to be performed
  Operand: Data/value/memory location on which the op code is going to work
Example: Add R1, R2
  Add: Op code
  R1 and R2: Operands
  R2: Source, R1: Destination
  R2: Will remain unchanged, R1: May get modified (if R2 is not 0)

## Slide 19: Instruction Examples
  mov reg, reg/memory/constant
  mov memory, reg
  add reg, reg/memory/constant
  sub reg, reg/memory/constant
  cmp reg, reg/memory/constant
  and reg, reg/memory/constant
  or reg, reg/memory/constant
  not reg/memory

## Slide 20: The ‘x86’ Architecture

## Slide 21: Intel x86 Architecture – Basic Terms
x86: Instruction Set Architectures (ISA): Intel processors, 16-bit instruction set, later modified to 32-bit
x64: 64-bit architecture
Architecture | Meaning | Details about the name
x86 | 32-bit architecture | ‘86’ = Processor 8086
x64 | 64-bit architecture | ‘64’ = Number of bits

## Slide 22: Intel x86/X64 Architecture – Understanding
X86
  32-bit CPU = 32 wires between CPU and main memory (Address bus = 32 bits)
  2^32 = 4,294,967,295
  So, a 32-bit X86 processor can access ~4GB RAM locations
  Also, at a time, 32 bits of data will be read from memory (Data bus = 32 bits)
X64
  64-bit CPU = 64 wires between CPU and main memory (Address bus = 64 bits)
  2^64 =18.4 exabyte memory locations can be accessed (See next slide)
  Also, at a time, 64 bits of data will be read from memory (Data bus = 64 bits)

## Slide 23: Measuring Bits-Bytes

## Slide 24: Overview of x86 Data Types
Byte
Word
Doubleword
Quadword
Bit
Nibble
8
16
32
64
1
4

## Slide 25: Ranges of Important Data Types
System | Range | Power of 2 | How many bytes?
Byte | 0-255 | 0 to 28 - 1 | 1
Word | 0-65,535 | 0 to 216 – 1 | 2
Doubleword | 0-4,294,967,295 | 0 to 232 – 1 | 4
Quadword | 0-18,446,744,073,709,551,615 | 0 to 264 – 1 | 8

## Slide 26: Basic x86 Microcomputer Design

## Slide 27: Reading from Memory: Clock Cycles
Cycle 1: Address bits of the memory bits are placed on the address bus
Cycle 2: Read line is set to 0 (Low) to indicate that this is a memory read operation
Cycle 3: CPU waits one cycle to give memory, time to respond
Cycle 4: Memory controller places the data and Read line becomes 1, to indicate to the CPU to read the data on the data bus

## Slide 28: Addressing Modes

## Slide 29: Addressing Modes
Addressing mode: Decides how to identify the operands
Types: Register, Immediate, Direct, Indirect, Indexed
Allows more flexibility to the programmer, since the operands can be in the registers, memory, or in a memory location pointed to by another memory location
Drawback: More complexity in instructions

## Slide 30: Register Addressing Mode
Register addressing: Operands are in the CPU registers
Example: add ax, bx
Fastest
Problem: Upper limit based on number of registers
Program to add two numbers
mov ax, 03h
mov bx, 05h
add ax, bx

## Slide 31: Immediate Addressing
Immediate addressing: Operand is a constant
Example: add ax, 25
No memory access needed
Limited use
Program to add a constant to a register that already contains some value
mov ax, 03h
add ax, 05h

## Slide 32: Direct Addressing Mode
Direct addressing: Operand’s memory address is used
Example: mov ax, [1000]
Simplest
Limited by register and memory size
Program to add a value stored at memory address 1000 into a register
mov ax, 03h
mov [1000h], 05h
add ax, [1000h]

## Slide 33: Indirect Addressing Mode
Indirect addressing: Actual value is at a memory address, and address value is in a register
Example: mov ax, [bx]
Complex and slow
Program to read the value at a memory address stored in a register
mov ax, 03h
mov [1000h], 05h
mov bx, 1000h
add ax, [bx]

## Slide 34: Indexed Addressing Mode
Indexed addressing: Actual value is at a memory address, and address value plus an index is in a register
Example: mov ax, [1000+bx]
Use: Arrays, pointers, records, and other data structures