## Slide 1: Hexadecimal to Binary Conversion
If you remember the previous table, we can simply convert each hexadecimal digit to its 4-bit binary equivalent
Examples

## Slide 2: Binary to Hexadecimal Conversion
Now do the opposite!
Examples

## Slide 3: Exercise
Find hexadecimal equivalent of
Find hexadecimal equivalents of

## Slide 4: Exercise
Find binary equivalents of

## Slide 5: Hexadecimal to Decimal Conversion
Convert F8E6 in hexadecimal to decimal
Exercise: Now convert 63,718 in decimal to Hex. Do you get F8E6?

## Slide 6: Solution
16 63718 6 in decimal .... 6 in hex
16 3982 14 in decimal .... E in hex
16 248 8 in decimal .... 8 in hex
16 15 15 in decimal .... F in hex
0
63718 in decimal = F8E6 in hex

## Slide 7: Decimal to Hexadecimal Conversion
Convert 3479 in decimal to hexadecimal

## Slide 8: Conversion: Summary
Binary-to-Decimal: 8-4-2-1 method or multiply by 2^0, 2^1 etc from RHS
Decimal-to-Binary: Divide by 2, write quotient and remainder, finally write remainder in the reverse order
Hex-to-Decimal: multiply by 16^0, 16^1 etc from RHS
Decimal-to-Hex: Divide by 16, write quotient and remainder, finally write remainder in the reverse order
Binary-to-Hex: Write hex symbol for every four bits
Hex-to-Binary: Write 4-bit binary representation for every hex symbol

## Slide 9: BCD Numbers
Binary-coded-Decimal (BCD) numbers express each decimal digit as a sequence of four bits
Example: Decimal number 2945 in BCD is 0010 1001 0100 0101

## Slide 10: BCD to Decimal
Read four bits at a time and write the corresponding decimal digit

## Slide 11: The ASCII Code
Computers need to deal with numbers, alphabets, and other symbols
But they only understand binary (0 and 1)
American Standard Code for Information Interchange (ASCII) = Code to map symbols to binary values
Initially 7-bit, then modified to 8-bit (Extended ASCII)

## Slide 12: The ASCII Table

## Slide 13: Unicode
Unicode is a universal character encoding standard
This standard includes roughly 100000 characters to represent characters of different languages
While ASCII uses only 1 byte the Unicode uses 4 bytes to represent characters
Hence, it provides a very wide variety of encoding

## Slide 14: Binary Arithmetic

## Slide 15: Binary Addition
Rules of binary addition
0 + 0 = 0
0 + 1 = 1
1 + 0 = 1
1 + 1 = 10
1 + 1 + 1 = 11

## Slide 16: Binary Addition Example
Add two binary numbers: 11100 and 11010
Here, 1 + 1 + 1 (carry) produces 11, recorded as 1 with a carry of 1 to the next higher column

## Slide 17: Binary Subtraction
Rules of binary subtraction
0 – 0 = 0
1 – 0 = 1
1 – 1 = 0
10 – 1 = 1

## Slide 18: Binary Subtraction Example
Computers use different techniques for binary subtraction, as we will discuss soon

## Slide 19: Signed Binary Numbers
Negative decimal numbers are -1, -2, -3, etc
For binary numbers, positive sign is 0 and negative sign is 1, so:
  In binary 0001 means +1 and 1001 means -1
  In binary 0010 means +2 and 1010 means -2, etc
Such numbers are called signed binary numbers or sign-magnitude numbers
Example: Express the following as 16-bit signed binary numbers:
  +7, -7, +25, -25
Solution: Next slide